Opentrons Developer Skinny Guide	JY 09/28/20

Overview:
To design protocols effectively you need to break it down into steps, instead of doing it all at once. There is both dry lab design of the protocol in GUI/python, and then testing of it by observing the robot as it goes through the steps. An efficient workflow is:
- design the protocol using the GUI
- edit the protocol in python to make it adaptable for different #s of samples
- test it on water experimentally and observe; iterate until satisfied
- test on real samples and assay result to ensure quality.

1. GUI Design
Go to this website: https://designer.opentrons.com/
- create a new file
- input the liquids in your protocol (ie wash buffer,buffer A, buffer B)
- Layout the plate deck – remember you need to account for space for tip boxes
- Begin designing the protocol stepwise – just design it for one full 96 well plate. Individual logic will be later.
- Remember the steps specify mixing at both aspirate and dispense as well as tip logic, so do that. You can also just edit this later in python.
- Export File

2. Editing in Python
Go to this website to get API: https://docs.opentrons.com/v2/
- edit the workflow with any steps that you may have forgotten/needed to edit
- write in logic for handling increments of smples (ie 8 or 12 at a time). Note that if you only have multichannels attached you will only be able to do increments of 8 or 12.
- Make an interface pop up to inform the user what they need to do
- COMMENT!

3. Testing on Water
- Turn on the robot and remove modules from deck as necessary. Modules have their own power.
- Load the protocol using the OT desktop program
- Calibrate the instrument to your protocol
- Setup the plate deck as specified and liquids with water like you were doing the real assay. Use food dye as necessary.
- Run protocol and make notes where it is going wrong/can be improved.
- Repeat step 3 until finalized.

4. Biological Sample Testing
- Prepare the protocol using the smallest increment with biological samples/buffers.
- Run the protocol. Observe.
- Harvest and assay for efficiency.